## Slide 1
SAVE THE DATE
LUSTRE USER GROUP (LUG) 2020
JUNE 9 - 12, 2020
BERKELEY, CALIFORNIA
Hosted by LBNL/NERSC,
UC Berkeley Research IT,
and OpenSFS

## Slide 2
NERSC's Perlmutter System:
Deploying 30 PB of all-NVMe Lustre at scale
Glenn K. Lockwood
Kirill Lozinskiy
Kristy Kallback-Rose
Storage Systems Group National Energy Research Scientific Computing Center Lawrence Berkeley National Laboratory

## Slide 3: NERSC’s 2020 System: Perlmutter
Cray Shasta
  3x to 4x capability of Cori
  GPU-accelerated and CPU-only nodes
  Cray Slingshot interconnect
Single-tier, all-flash Lustre
  Cray E1000F-based system
  30 PB usable capacity
  ≥ 4.0 TB/s sustained bandwidth
  ≥ 7,000,000 IOPS (read and write)
  ≥ 3,200,000 file creates/sec
CPU-only nodes
AMD Epyc™
Milan CPUs
CPU-GPU nodes
Future NVIDIA GPUs
Tensor Cores
All-flash platform integrated storage
Login nodes
High-memory workflow nodes
“Slingshot” Interconnect Ethernet Compatible
External file systems & networks

## Slide 4: NERSC-Cray Collaboration
How much capacity? How much endurance?
DNE, DOM configuration?
ldiskfs or ZFS? Which meets performance spec?
Above: optimal MDT capacity for different DOM component sizes.
See Lockwood et al.,"A Quantitative Approach to Architecting All-Flash Lustre File Systems" in High Performance Computing, Chapter 16. https://doi.org/10.1007/978-3-030-34356-9_16

## Slide 5: Cray's work on all-NVMe Performance - IOR
Cray's Test OSS | Perlmutter (Cray E1000F)
24c AMD Rome | ≥24c AMD Rome
2x EDR (100G) | ≥2x Slingshot (200G)
PCIe Gen3 SSDs | PCIe Gen4 SSDs
Cray Lustre (community + forward-ported patches) | 
Declustered RAID6 8+2+1 (GridRAID) | 
22 GB/s/OSS read
18 GB/s/OSS write
440 KIOPS/OSS read
30 KIOPS/OSS write

## Slide 6: Thank you—and we're hiring! Ask any NERSC staff for more info