## Slide 1
GPU Computational Screening of Carbon Capture Materials
J Kim1, A Koniges1, R Martin1, M Haranczyk1, J Swisher2 and B Smit1,2
1Berkeley Lab (USA), 2Department of Chemical Engineering, University of California, Berkeley (USA)
New GPU cluster Dirac at NERSC
(44 Fermi Tesla C2050 GPU cards)
448 CUDA cores, 3GB GDDR5 memory, PCIe x16 Gen2, 55 (1030) GFLOPS peak DP(SP) performance
144 GB/sec memory bandwidth
Dirac node: 2 Intel 5530 2.4 GHz, 8MB cache, 5.86 GT/sec QPI Quad-core Nehalem, 24GB DDR3-1066 Reg ECC memory
More than 500 cores
Optimized for SIMD (same-instruction-multiple-data) problems
Less than 20 cores
Designed for general programming
ALGORITHM: Characterize Large Database of Carbon Capture Materials
CPU
GPU
Control
Logic
ALU
ALU
Cache
DRAM
DRAM
Step 1: Energy Grid Construction
Step 2: Pocket blocking
Step 3: Monte Carlo Widom Insertion
application: Carbon Capture and Storage
Project Goal: reduce the cost of separating CO2 molecules from power
plant flue gases (46 Energy Frontier Research Centers established by the DOE)
Candidates for Carbon Capture: zeolites, metal-organic frameworks
Over a million hypothetical zeolite structures: how to determine the optimal structure?
Develop GPU code to accelerate screening a large database of carbon capture materials
Henry Coefficients (KH): characterize selectivity of material at low pressure (used as an initial screening quantity for zeolites)
LTA zeolite
MFI zeolite
Test insert gas molecule at each grid point and calculate its energy
0.1 Angstroms grid size (10million+ grid points, GPU DRAM)
Framework atoms (< 2000), keep data in fast GPU memory
Number of GPU threads = number of grid points
Lennard-Jones + Coulomb potentials with periodic boundary conditions
X: framework atoms
x
x
x
x
x
x
x
Thread 0
Thread 1
Thread 2
Thread 3
…
Motivation: need to block inaccessible regions (pockets) within the framework
Set threshold energy value such that accessible if exp(-Ei) > exp(-15kBT)
Flood fill algorithm to detect pockets
Test insert a gas molecule in simulation box (CH4: one insertion, CO2: three insertions)
Check for (a) out of boundary (redo) and (b) inside pocket sphere
Interpolate energy values from grid points
Accumulate Boltzmann factor and repeat
Utilize CURAND Library to generate random numbers
Blocking spheres
(a)
(b)
Periodic Unit Cell
(1)
(2)
(3)
(1) and (2) are disconnected and thus inaccessible (block)
(3) forms a channel (accessible)
Periodic, Non-orthogonal
Unit Cell
GPU racks (NERSC Dirac)
Performance Results
Simulations of IZA structures: 190+ experimentally known zeolites
CH4: 2.2 seconds/zeolite
CO2: 31.8 seconds/zeolite
64(72)% of wall time spent in CPU pocket blocking
The code is compute bound (50x improvement from CPU single core implementation)
Successfully computed 120,000+ Henry coefficients for CH4 inside hypothetical zeolites: 5 GPUs, less than 1 day of wall time
Local Henry coefficient color map indicates the regions within the zeolite that contribute most to the overall Henry coefficients
Henry coefficients (IZA)
Local Henry coefficients (MFI)
Future work
acknowledgment
Adsorption Isotherm calculations using GPU for CO2
Determine good parallelization strategy for the adsorption isotherms
Henry coefficient calculations for ZIFs, and metal-organic frameworks
SM14
GPU Tesla C2050 14 SMs
…
GCMC
P = 1 atm
GCMC
P = 100 atm
GPU Adsorption Isotherm
This work was supported by the Director, Office of Science, Advanced Scientific Computing Research, of the U.S. Department of Energy under Contract No. DE-AC02-05CH11231.
Architecture: NERSC Dirac GPU Cluster
SM2
SM1